## Slide 1
4.1
Under graduate (2016)
Girma Adam (M.Tech)
Chapter Four
Combinational
logic circuits

## Slide 2
4.2
Topics discussed in this section:
Cont’d..
Introduction
Adders
Subtractors
Binary code conversion
Magnitude comparator
Decoders
Encoders
Multiplexers and Multiplexer tree

## Slide 3
4.3
Introduction
Basically the digital Circuits are divided in to two broad categories
  Combinational Circuits
  Sequential Circuits
A Combinational circuits consists of logical gates whose output at any time are depending on the present combination of inputs.
A block diagram of a combinational circuit is as shown below

## Slide 4
4.4
Cont’d..
The design of combinational circuits starts from the outline of the problem and ends in a logical circuit diagram, or set Boolean functions from which the logic diagram can be obtained.
The procedure involves the following steps:-
  The problem is stated
  The number of both input and output variables required are determined
  Both input and output variables are assigned letter symbols
  Te truth table that defines the required relationships between input and outputs are derived.

## Slide 5
4.5
Cont’d..
    The simplified Boolean function for each output is obtained.
    The logic diagram is drawn.
  A practical design method have to consider the following
  requirements:-
  1. Minimum number of gates
  2. Minimum number of inputs to the gates
  3. Minimum propagation delay
  4. Minimum number of interconnection
  5. High Speed of processing
  6. Less Complexity

## Slide 6
4.6
ADDERS
The most basic arithmetic operation is the addition of two binary digits.
This simple addition consist of four possible elementary operations
A Combinational circuits that performs the addition of two bits is
called a Half-adder.
A Combinational circuits that performs the addition of three
bits(two significant bits and a previous carry) is called Full-adder.

## Slide 7
4.7
Half-adder
The half-adder can be used to add together the two least significant bits A and B of two numbers, where there is no input carry.
The block diagram of a half-adder is shown below

## Slide 8
4.8
Cont,d..
Formulate a truth table to identify exactly the function of the half-adder.
The simplified Boolean functions for the two outputs can be obtained directly from the truth table.
The simplified expressions for S and C are:-

## Slide 9
4.9
Cont’d..

## Slide 10
4.10
Full-adder
A half-adder has only two inputs and there is no provision to add
a carry coming from the lower order bits when multibit addition is
performed.
For this purpose, a third input terminal is added and this circuits
(full -adder) is used to add An,Bn,Cn-1.
where
An and Bn are the nth order bits of the number A and B respectively.
Cn-1 is the carry generated from the addition of (n-1) the order bits

## Slide 11
4.11
Cont,d..
The truth table of full-adder and the k-map for simplification of
outputs Sn and Cn are given below

## Slide 12
4.12
Cont’d..
This implementation uses the following Boolean expressions

## Slide 13
4.13
Cont’d...
The Sn output from the second half-adder is the exclusive-OR of Cn-1 and the output of the first half-adder, giving
Carry

## Slide 14
4.14
Cont’d...

## Slide 15
4.15
Full-adder from half-adders

## Slide 16
4.16
Parallel adder
Two or more full-adders are connected to form parallel binary adders.
The carry output signal from one stage propagates to the carry input of the next stage

## Slide 17
4.17
Cont,d..
Example.1:- Determine the sum generated by the 3-bit parallel adder and show the intermediate carriers when the binary number 101 and 011 are being added ?
Solution

## Slide 18
4.18
A 4-bit parallel binary adder
Exercise 1:- Show how adders can be connected to form an 8-bit parallel adder, and show the output bits for the following input binary numbers ? 10111001 and 10011110

## Slide 19
4.19
Subtractors
Half-Subtractor:- a logical circuit for the subtraction of B from A, where A and B are 1-bit numbers is referred to as a half-Subtractor.
The truth table of half-Subtractor is :-
Here A and B are two inputs and D (difference) and C(borrow) are the two outputs

## Slide 20
4.20
Cont’d...
From the truth table, the logical expression for D and C are obtained
The logical diagram of half-Subtractor using gates is shown below

## Slide 21
4.21
Cont’d..
Full-Subtractor:- Just like a full-adder we require a full-Subtractor for performing multi bit subtraction ,
A full-Subtractor will have three inputs, An ,Bn and Cn-1 (borrow from the previous stage) and two out puts Dn (difference) and Cn (borrow).
The truth table of Full-subtractor is :-

## Slide 22
4.22
Cont’d..
Inputs |  |  | Outputs | 
An | Bn | Cn1 | Dn | Cn
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
The truth table of full-Subtractor and the k-map for simplification of
outputs Dn and Cn are given below

## Slide 23
4.23
Cont’d..
This implementation uses the following Boolean expressions

## Slide 24
4.24
Cont’d..
The full – Subtractor logic Circuit diagram

## Slide 25
4.25
Binary Subtractor using 2’s complement
The Subtrcation A – B can be done by taking the 2’s complement of B and adding it to A because A- B = A + (-B) = A+2’sB.
It means if we use the inverters to make 1’s complement of B (connecting each Bi to an inverter) and then add 1 to the least significant bit (by setting carry C0 to 1) of binary adder, then we can make a binary subtractor.

## Slide 26
4.26
4 bit 2’s complement Subtractor

## Slide 27
4.27
Binary Conversion
The availability of a large variety of codes for the same discrete elements of information results in the use of different codes by different digital systems.
It is sometimes necessary to use the output of one system as input to another , at this condition a conversion circuit is inserted between the two systems, if each uses different codes for the same information.
Thus a code converter is a circuit that makes the two systems compatible even though each system uses a different binary code.

## Slide 28
4.28
Cont’d..
The design procedure of code converters will be illustrated by means of a specific examples:-
Binary to Gray code converter
The truth table of a 4-bit binary to gray code converter is given below:-
Binary codes |  |  |  | Gray codes |  |  | 
B3 | B2 | B1 | B0 | G3 | G2 | G1 | G0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0

## Slide 29
4.29
Cont’d..
Binary codes |  |  |  | Gray codes |  |  | 
B3 | B2 | B1 | B0 | G3 | G2 | G1 | G0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0

## Slide 30
4.30
Cont’d..

## Slide 31
4.31
Cont’d..
This implementation uses the following Boolean expressions

## Slide 32
4.32
Cont’d..
2. Gray to Binary code converter
The truth table of a 4-bit Gray to binary code converter is given
below:-
Gray codes |  |  |  | Binary codes |  |  | 
G3 | G2 | G1 | G0 | B3 | B2 | B1 | B0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1

## Slide 33
4.33
Cont’d..
Gray codes |  |  |  | Binary codes |  |  | 
G3 | G2 | G1 | G0 | B3 | B2 | B1 | B0
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1

## Slide 34
4.34
Cont’d..

## Slide 35
4.35
Cont’d..
This implementation uses the following Boolean expressions
and logic diagram

## Slide 36
4.36
Cont’d..
Exercise
Convert the binary number 0101 to Gray code with
exclusive –OR gates
2. Convert the Gray code 1011 to binary with
exclusive –OR gates
Solution

## Slide 37
4.37
Magnitude comparator
A magnitude comparator is a combinational circuit that compares
two numbers A and B, and determines their relative magnitudes.
The outcome of the comparison is specified by three binary
variables that indicate whether A> B, A=B or A<B.
Exclusive-OR gate can be used as a basic comparator
Equality
Exclusive-OR gate as 1-bit comparator

## Slide 38
4.38
Cont’d..
Exclusive-OR gate as 2-bit comparator
The output is 1 when Ao=Bo and A1=B1,

## Slide 39
4.39
Cont’d..
Exclusive-OR gate as 4-bit comparator
Detects one of three conditions
Only one output will be High at any one time
- A greater than B (A > B)
- A equal to B (A = B)
- A less than B (A < B)

## Slide 40
4.40
Cont’d..
The two numbers will be equal if all pairs of significant digits
are equal, that is, A3 = B3, A2 = B2,A1 = B1 and A0 = B0.
To determine an inequality of binary number A and B, starting from the most significant position in each number. The following condition are possible
1. If A3 = 1 and B3 = 0 , number A > B
2. If A3 = 0 and B3 = 1, number A <B
3. If A3 = B3 , then you must examine the next lower bit position for an inequality.
The comparison continues until a pair of unequal digits is reached.

## Slide 41
4.41
Cont’d..
Example:- Apply each of the following sets of binary numbers to the comparator circuit and determine the output by following the logical levels through the circuit
a) 10 and 10 b) 11 and 10
Solution

## Slide 42
4.42
Cont’d..
Example:- Determine the A=B, A >B and A < B outputs for the
input numbers shown on the comparator circuit ?
Solution
The number A is greater than B, A > B output is high and the other output are low

## Slide 43
4.43
Designing Comparators Functionally
One bit comparator

## Slide 44
4.44
Cont’d..
Design a comparator for 2 bit binary numbers A
(A1A0) and B (B1B0) we do the following steps:
For a 2-bit comparator we have four inputs A1A0 and B1B0 and three output
1. E ( is 1 if two numbers are equal)
2. G (is 1 when A > B) and
3. L (is 1 when A < B)
The circuit, for comparing two n-Bit numbers, has 2n inputs &
22n entries in the truth table.
For 2-Bit numbers, 4-inputs & 16-rows in the truth table.

## Slide 45
4.45
Cont’d..
Truth Table of 2-Bit Magnitude Comparator

## Slide 46
4.46
Cont’d..

## Slide 47
4.47
Cont’d..

## Slide 48
4.48
Cont’d..

## Slide 49
4.49
Cont’d..

## Slide 50
4.50
Combined

## Slide 51
4.51
Decoder
A decoder is a combinational logic circuit that accepts a set of inputs that represents a binary number and activates only the output that corresponds to the input number.
In its general form, a decoder has n input lines to handle n bits and form one to 2 n output lines to indicate the presence of one or more n-bit combinations.
The decoder presented here are called n-to-m line decoders where m ≤ 2n .
The general Block diagram of a Decoder circuit

## Slide 52
4.52
Cont’d..
# There are 2N possible input combinations, from A0 to AN1.
For each of these input combinations only one of the M outputs will be active HIGH (1), all the other outputs are LOW (0).

## Slide 53
4.53
Cont’d..
The basic binary function
If an active-LOW output (74138, one of the output will low and the rest will be high) is required for each decoded number, the entire decoder can be implemented with
    NAND gates
    Inverters
If an active-HIGH output (74139, one of the output will high and the rest will be low) is required for each decoded number, the entire decoder can be implemented with
    AND gates
    Inverters

## Slide 54
4.54
Cont’d..
Example: 1 Decoding logic for the binary code 1001 with an
active-HIGH output.
Solution

## Slide 55
4.55
Decoder with Enable Line
Decoders usually have an enable line,
Enabling permits an input signal to pass through to an output
Disabling blocks an input signal from passing through to an output, replacing it with a fixed value.
If enable=0 , decoder is off. It means all output lines are zero
If enable=1, decoder is on and depending on input, the corresponding output line is 1, all other lines are 0

## Slide 56
4.56
Cont’d..
Example.2: 2-to-4 line decoder (with enable input)-active
Low output
Solution

## Slide 57
4.57
Cont’d..
For example if the number of input is n=3 the number of output lines can be m=23 . It is also known as 1 of 8 because one output line is selected out of 8 available lines:
The decoder presented here are called n-to-m line decoders where m ≤ 2n

## Slide 58
4.58
Cont’d..
Their purpose is to generate the 2n or less minterms of n input variables.
Consider the 3-to-8 line decoder , the three inputs are decoded in to eight outputs, each output representing one of the minterms of the 3-input variables.

## Slide 59
4.59
Cont’d..
The truth table of a 3-to-8 line decoder

## Slide 60
4.60
Cont’d..

## Slide 61
4.61
Cont’d…
This binary port address is decoded and the appropriate decoder output is activated to enable the I/O port.

## Slide 62
4.62
BCD-to-Decimal Decoder
The elements of information in this case are the ten decimal digits represented by the BCD code.
The code itself has four bits
This will gives a 4-to-10 line BCD –to-decimal decoder.

## Slide 63
4.63
Cont’d..
The truth table of BCD –to-Decimal decoder
inputs |  |  |  |  | outputs |  |  |  |  |  |  |  | 
A3 | A2 | A1 | A0 | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7 | D8 | D9
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 64
4.64
Cont’d..

## Slide 65
4.65
BCD-7segment decoders/drivers
Most digital equipment has some means for displaying information
in a form that can be understood by the user. This information is
often numerical data but also be alphanumeric.
One of the simplest and most popular methods for displaying
numerical digits uses a 7-segment configuration to form digital
characters 0 to 9 and some times the hex characters A to F

## Slide 66
4.66
Cont’d..
One common arrangements uses light-emitting diodes (LED's) for
each segment. By controlling the current through each LED, some
segments will be light and others will be dark so that desired
character pattern will be generated.
There are two types of 7segment LED displays;
A) common - anode
B) common  cathode

## Slide 67
4.67
Cont’d..
In commonanode, the anode of all of the LEDs are tied together to
positive of the power supply (Vcc) as shown

## Slide 68
4.68
Cont’d..

## Slide 69
4.69
Cont’d..
Example: 1

## Slide 70
4.70
Cont’d..

## Slide 71
4.71
Cont’d..
In common cathode, the cathode of all of the LEDs are tied together to positive of the power supply (Vcc) as shown

## Slide 72
4.72
Cont’d..

## Slide 73
4.73
Cont’d..

## Slide 74
4.74
Cont’d..

## Slide 75
4.75
Cont’d..
a = A + B D + C + B' D'
b = C' D' + C D + B'
c = B + C' + D
d = B' D' + C D' + B C' D + B' C + A
e = B' D' + C D’
f = A + C' D' + B D' + B C'
g = A + C D' + B C' + B' C

## Slide 76
4.76
Cont’d..

## Slide 77
4.77
Cont’d..

## Slide 78
4.78
Cont’d..
Example.1. Design and implement a logic diagram for a Boolean function given by a truth table below using a 3-to-8 decoder
Truth table:
Solution
Minterms:
  F=m(3,5,6,7)
Implementation using decoder:
A B C F
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 1
0
1
2
3
4
5
6
7
A
B
C
2
1
0
F
Indicate MSB, LSB

## Slide 79
4.79
Cont’d..
Example.2.Can you design and implement a Boolean Function given below using a 2-to-4 decoder with enable input and an OR gate?
Solution
Yes, Using a 2-to-4 decoder with enable input and an OR gate:
F=C(AB+A’B’)
F=C(AB+A’B’) = ABC + A’B’C
EN

## Slide 80
4.80
Cont’d..
Example.3. a 7-segment decoder drives the display in figure below. If the waveforms given below are applied as input, determine the sequence of digits that appears on the display ?
Solution

## Slide 81
4.81
Encoder
An encoder is a combinational logic circuit that essentially performs a ‘’ reverse’’ process of decoder function.
Encoders can encode various symbols and alphabetic characters.
The process of converting from familiar symbols or number to a coded format is called encoding.
An encoder accepts an active level on one of its inputs representing a digit, such as a decimal or octal and converts it to a coded output, such as BCD or Binary

## Slide 82
4.82
Cont’d..

## Slide 83
4.83
Decimal-to-BCD encoder
A decimal-to-BCD encoder
  Inputs: 10 bits corresponding to decimal digits 0 through 9, (D0, …, D9)
  Outputs: 4 bits with BCD codes
  Function: If input bit Di is a 1, then the output (A3, A2, A1, A0) is the BCD code for i,

## Slide 84
4.84
Cont’d..

## Slide 85
4.85
Cont’d..
  A3 = D8 + D9
  A2 = D4 + D5 + D6 + D7
  A1 = D2 + D3 + D6 + D7
  A0 = D1 + D3 + D5 + D7 + D9
The Boolean Equation can be :-

## Slide 86
4.86
Multiplexer & Multiplexer tree
It is a combinational circuit that selects binary information from one of the input lines and directs it to a single output line
Usually there are 2n input lines and n selection lines whose bit combinations determine which input line is selected
Depending upon the digital code applied at the selector inputs one out of n data source is selected and transmitted to a single output channel.

## Slide 87
4.87
Cont’d..

## Slide 88
4.88
Cont’d..
MUX Types
  2-to-1 (1 select line)
  4-to-1 (2 select lines)
  8-to-1 (3 select lines)
  16-to-1 (4 select lines)

## Slide 89
4.89
Typical Application of a MUX

## Slide 90
4.90
Cont’d..

## Slide 91
4.91
Cont’d..
For example for 2-to-1 multiplexer
1. if selection S is zero then I0 has the path to output and
2. if S is one I1 has the path to output

## Slide 92
4.92
Cont’d..
Truth table for 2-to-1 multiplexer
For 4-to-1 multiplexer

## Slide 93
4.93
Cont’d..
Truth table for 4-to-1 multiplexer
Derive the logical expression for the output in terms of the
data input and the select line
The output is equal to Do only if S1 = 0 and So = 0 : Y=DoS1So
The output is equal to D1 only if S1 = 0 and So = 1 : Y=D1S1So
The output is equal to D2 only if S1 = 1 and So = 0 : Y=D2S1So
The output is equal to D3 only if S1 = 1 and So = 1 : Y=D3S1So

## Slide 94
4.94
Cont’d..
The Boolean expression of the input selected (y)
The logic diagram of 4-to-1 multiplexer

## Slide 95
4.95
Cont’d..
Example.1. the data input and data-select waveforms in figure below are applied to the 4-to-1 multiplexer. Determine the output waveform in relation to the inputs ?
Solution

## Slide 96
4.96
Multiplexer tree
Pin diagram and logical symbol for the 74LS151 8-input data
selector/multiplexer.
A LOW on the Enable input allows the selected input data to pass through to the output. A HIGH on the Enable input prevents data from going through to the output; i.e, it disables the multiplexer.

## Slide 97
4.97
Cont’d..
Example.1. Design 16:1 multiplexer using 8:1 multiplexer ?
Solution
Exercise.1. Design 32:1 multiplexer using 8:1 and 4:1 multiplexer ?

## Slide 98
4.98
Boolean function Implementation
The multiplexing function can conveniently be used as a logic
element in the design of combinational circuits.
For using the multiplexer as a logic element, either the truth
table or one of the standard forms of logical expression must be
available.
The design procedure is given below
Identify the decimal number corresponding to each minterm in the expression.
The input lines corresponding to these numbers are to be connected to logic 1 level.
All other input lines are to be connected to logic o level.
The inputs are to be applied to select inputs

## Slide 99
4.99
Cont’d..
Example.1. Implement the logic function specified in truth table below by using a 74LS151 8-input data selector/multiplexer. Compare this method with a discrete logic gate implementation
Solution Y =Σm(1,3,5,6)

## Slide 100
4.100
Cont’d..

## Slide 101
4.101
Cont’d..
Another method for implementing Boolean function is using multiplexer
For doing that assume Boolean function has n variables. We have to use multiplexer with n-1 selection lines and
1- first n-1 variables of function is used for data input
2- the remaining single variable ( named z )is used for data input.
Each data input can be z, z’, 1 or 0. From truth table we have to find the relation of F and z to be able to design input lines.

## Slide 102
4.102
Cont’d..
Example.1. : f(A,B,C,D) = ∑(1,3,4,11,12,13,14,15)
Solution

## Slide 103
4.103
Cont’d..
Example.2.: Implement the logic function in truth table below by using 74LS151 8-input data selector/multiplexer. Compare this method with a discrete logic gate ?

## Slide 104
4.104
Cont’d..
Solution

## Slide 105
4.105
Demultiplexer
A demultiplexer basically reverse the multiplexing function. It takes digital information from one line and distributes it to a given number of outputs. For this reason the demultiplexer is also know as data distributor.

## Slide 106
4.106
Cont’d..
DEMUX Types
  1-to-2 (1 select line)
  1-to-4 (2 select lines)
  1-to-8 (3 select lines)
  1-to-16 (4 select lines)

## Slide 107
4.107
Typical Application of a DEMUX

## Slide 108
4.108
Cont’d..
For example for 1-to-4 De-Multiplexer (DEMUX)

## Slide 109
4.109
Cont’d..
Example.1. The serial data-input wave form(data in) and data-select inputs (So and S1) are as shown below. Determine the data-output waveforms for the 1-to-4 demultiplexer ?
Solution